## Slide 1: Calculating Termiticide Usage

## Slide 2
What do we need to know to be able
to calculate the amount of termiticide
to use on a subterranean termite job?

## Slide 3
If treating adjacent to a foundation wall, we need to know:
the length of that foundation wall to be treated
the application rate to use = 4 gallons/10 linear feet/foot of
the depth of the footer from grade
As an example, if you are
treating only one side of the foundation wall (as in a
Defined Soil Treatment), what is the length of that wall?
What is the rate of application to the soil along that foundation wall?
What is the depth of the footer? (the distance from grade to the footer)
X
X
=
Gallons of
termiticide needed to
treat soil
along wall
As an example, if the foundation wall is 90 long, the application rate is 4 gallons/10 linear feet and the depth of the footer is 2 feet deep, then…
90
.4
X
X
2
=
72
gallons

## Slide 4
If treating in voids of a foundation wall, we need to know:
the length of that foundation wall to be treated
the number of voids to be treated
the application rate to use = 2 gallons/10 linear feet per void (2/10 = .2 gallons/lin. ft.)
What is the length of the foundation wall that has voids to be treated?
How many sets of voids are there along the foundation wall to be treated?
What is the application rate to treat each void present?
Gallons of
termiticide needed to
treat voids of foundation wall
X
X
=
As an example, if you are treating the voids of a triple brick wall that is 75 feet long, the application rate is 2 gallons/10 linear feet and there are 2 voids, then…
75
X
2
X
.2
=
30
gallons

## Slide 5
If treating an area of soil to be covered by a slab on a pretreat, you need to know:
the square footage of the area to be treated (length x width)
whether the substrate is soil or is a gravel/rock fill
the application rate = 1 gallon/10 sq. ft. (1/10 = .1) if the substrate is soil and = 1.5 gallons/10 sq. ft. (1.5/10 = .15) if the substrate is gravel or rock fill
What is the square footage of the area to be treated?
X
What is the application rate to treat the soil or the gravel/rock fill substrate present?
Gallons of
termiticide needed to
treat soil to be covered by a slab
=
As an example, if you are treating soil to be covered by a slab that will be 25’ X 80’, the application rate will .1 gallon/square foot
25’ X 80’ = 2,000 sq. ft.
X
.1
=
200
gallons

## Slide 6
You may have 10 to 15 termiticide calculation word problems on your WDO exam, but don’t fret…
It’s not difficult to calculate the amount of termiticide to use if you read the question and then visualize the problem and treatment.
So let’s calculate the amount of termiticide to use on a few word problems.

## Slide 7: How many gallons of finished dilution of termiticide would you apply to treat the voids of a brick veneer/hollow block foundation wall that is 83 feet long?

## Slide 8: How many gallons of finished dilution of termiticide would you apply to treat the voids of a brick veneer/hollow block foundation wall that is 83 feet long?
What is the first thing you need to do in
order to determine the answer to the
question above?
“VISUALIZE THE PROBLEM”

## Slide 9: How many gallons of finished dilution of termiticide would you apply to treat the voids of a brick veneer/hollow block wall that is 83 feet long?
Draw a picture of the wall (a view from the side) to determine how many rows of voids are to be treated.
footer
2 rows of voids
Now that we have established that two
rows of voids must be treated, what is
the application rate for void treatment?
2 gallons per 10 linear feet
2 gallons/10 lin. ft. = 0.2 gal./lin. ft.
Two (2) voids must be treated.
Each void is treated with 0.2 gal./lin. ft.
0.2 gal./lin. ft. + 0.2 gal./lin. ft. = 0.4 gal./lin. ft.

## Slide 10: How many gallons of finished dilution of termiticide would you apply to treat the voids of a brick veneer/hollow block wall that is 83 feet long?
footer
83 linear feet
x 0.4 gal./lin. ft.
33.2 gallons
0.2 gal./lin. ft. 0.2 gal./lin.ft. = 0.4 gal./lin. ft. X 83 lin. ft. = 33.2 gallons of diluted termiticide
+

## Slide 11: How many gallons of finished dilution of termiticide would you apply to treat the voids of a double brick wall that is 92 feet long?

## Slide 12: How many gallons of finished dilution of termiticide would you apply with a Comprehensive Soil treatment to treat the voids of a double brick wall that is 92 feet long?
What is the first thing you need to do in
order to determine the answer to the
question above?
“VISUALIZE THE PROBLEM”

## Slide 13: How many gallons of finished dilution of termiticide on a Comprehensive Soil treatmtent would you apply to treat the voids of a double brick wall that is 92 feet long?
Draw a picture of the wall (one side view) to determine how many rows of voids are to be treated.
footer
1 void
Now that we have established that one
row of voids must be treated, what is
the application rate for void treatment?
2 gallons per 10 linear feet
2 gallons/10 lin. ft. = 0.2 gal./lin. ft.
One (1) void must be treated.
The void is treated with 0.2 gal./lin. ft.

## Slide 14: How many gallons of finished dilution of termiticide would you apply to treat the voids of a double brick wall that is 92 feet long?
footer
0.2 gal./lin. ft. x 92 linear feet = 18.4 gallons of diluted termiticide
92 linear feet
x 0.2 gal./lin. ft.
18.4 gallons

## Slide 15: How many gallons of finished dilution of termiticide would you apply on a Comprehensive Soil treatment to treat the voids and the soil on both sides of a double brick wall of a crawl space structure that is 65 feet long? The footer is one foot deep.

## Slide 16: How many gallons of finished dilution of termiticide would you apply on a Comprehensive Soil treatment to treat the voids and the soil on both sides of a double brick wall of a crawl space structure that is 65 feet long? The footer is one foot deep.
What is the first thing you need to do in
order to determine the answer to the
question above?
“VISUALIZE THE PROBLEM”

## Slide 17: How many gallons of finished dilution of termiticide would you apply on a Comprehensive Soil treatment to treat the voids and the soil on both sides of a double brick wall of a crawl space structure that is 65 feet long?
Draw a picture of the wall (a side view) to determine how the structure is to be treated.
footer
Drill &
Treat
1 void
(0.2 gal./
lin. ft.)
Trench
and
Treat
(0.4 gal./
lin. ft.)
Trench
and
Treat
(0.4 gal./
lin. ft.)
0.4 + 0.2 + 0.4 = 1.0 gal./lin. ft.
1’

## Slide 18: How many gallons of finished dilution of termiticide would you apply on a Comprehensive Soil treatment to treat the voids and the soil on both sides of a double brick wall of a crawl space structure that is 65 feet long?
footer
Drill &
Treat
1 void
(0.2 gal./
lin. ft.)
Trench
and
Treat
(0.4 gal./
lin. ft.)
Trench
and
Treat
(0.4 gal./
lin. ft.)
65 linear feet x1.0 gal./lin. ft.
65 gallons
1’
1 gallon/lin. ft. X 65 linear feet = 65 gallons of diluted termiticide

## Slide 19: How many gallons of finished dilution of termiticide would you apply on a Comprehensive Soil treatment to treat the voids of a hollow block wall, the soil adjacent to the outside foundation wall, and the soil under the slab that is adjacent to a 75 foot long exterior foundation wall of a crawl space?

## Slide 20: How many gallons of finished dilution of termiticide would you apply on a Comprehensive Soil treatment to treat the voids of a hollow block wall, the soil adjacent to the outside foundation wall, and the soil under the slab that is adjacent to a 75 foot long exterior foundation wall of a crawl space?
What is the first thing you need to do in
order to determine the answer to the
question above?
“VISUALIZE THE PROBLEM”

## Slide 21: How many gallons of finished dilution of termiticide would you apply on a Comprehensive Soil treatment to treat the voids of a hollow block wall, the soil adjacent to the outside foundation wall, and the soil under the slab that is adjacent to the exterior foundation wall of a crawl space structure that is 75 feet long?
footer
Drill &
Treat
1 void
(0.2 gal./
lin. ft.)
Drill
and
Treat
(0.4 gal./
lin. ft.)
Trench
and
Treat
(0.4 gal./
lin. ft.)
1’
1 gal./lin. ft. X 75 linear feet = 75 gallons of diluted termiticide
75 linear feet
x1.0 gal./lin. ft.
75 gallons

## Slide 22: How many gallons of finished dilution of termiticide would you apply on a Comprehensive Soil treatment to treat the voids of a hollow block foundation wall of a supported slab structure and the soil on both sides of the foundation wall that is 75 feet long? (exterior-footer depth = 1’, interior-footer depth = 3’)
What is the first thing you need to do in
order to determine the answer to the
question above?
“VISUALIZE THE PROBLEM”

## Slide 23: How many gallons of finished dilution of termiticide would you apply on a Comprehensive Soil treatment to treat the voids of a hollow block foundation wall of a supported slab structure and the soil on both sides of the foundation wall that is 75 feet long? (exterior-footer depth = 1’, interior-footer depth = 3’)
footer
Drill &
Treat
1 void
(0.2 gal./
lin. ft.)
Drill
and
Treat
(0.4 gal./
lin. ft./
ft. depth)
Trench
and
Treat
(0.4 gal./
lin. ft.)
1’
0.4 + 0.2 + 0.4 X 3 = 0.4 + 0.2 + 1.2 = 1.8 gallons/lin. ft.

## Slide 24: How many gallons of finished dilution of termiticide would you apply on a Comprehensive Soil treatment to treat the voids of a hollow block wall, the soil adjacent to the outside foundation wall, and the soil under the slab that is adjacent to the exterior foundation wall of a crawl space structure that is 75 feet long?
footer
Drill &
Treat
1 void
(0.2 gal./
lin. ft.)
Drill
and
Treat
(0.4 gal./
lin. ft./
ft. depth)
Trench
and
Treat
(0.4 gal./
lin. ft.)
1’
75 linear feet
x1.8 gal./lin. ft.
135 gallons

## Slide 25: How many gallons of finished dilution of termiticide would you apply on a Comprehensive Soil treatment to treat the voids of a hollow block wall and the soil adjacent to a 75 foot long exterior foundation wall of a basement structure?

## Slide 26: How many gallons of finished dilution of termiticide would you apply on a Comprehensive Soil treatment to treat the voids of a hollow block wall and the soil adjacent to a 75 foot long exterior foundation wall of a basement structure?
What is the first thing you need to do in
order to determine the answer to the
question above?
“VISUALIZE THE PROBLEM”

## Slide 27: How many gallons of finished dilution of termiticide would you apply on a Comprehensive Soil treatment to treat the voids of a hollow block wall and the soil adjacent to a 75 foot long exterior foundation wall of a basement structure?
Draw a picture of the wall (a side view) to determine how the structure is to be treated
4’ depth
0.4 gal./lin. ft. X 4 feet of depth = 1.6 gals./lin. ft.
0.2 gal./lin. ft.
1.6 gals./lin. ft. + 0.2 gal./lin. ft. = 1.8 gals./lin. ft.

## Slide 28: How many gallons of finished dilution of termiticide would you apply on a Comprehensive Soil treatment to treat the voids of a hollow block wall and the soil adjacent to the exterior foundation wall of a basement structure that is 75 feet long?
Draw a picture of the wall (a side view) to determine how the structure is to be treated
4’ depth
1.8 gals./lin. ft. x 75 linear feet = 135 gallons of diluted termiticide
75 linear feet
x1.8 gal./lin. ft.
135 gallons
0.2 gal/lin. ft.
0.4 gal./lin. ft.
X 4 feet of depth
1.6 gals./lin. ft.

## Slide 29: How many gallons of finished dilution of termiticide would you apply to treat the soil area to be covered by a slab that will be 40 feet wide by 150 feet long on a preconstruction treatment?

## Slide 30: How many gallons of finished dilution of termiticide would you apply to treat the soil area to be covered by a slab that will be 40 feet wide by 150 feet long on a preconstruction treatment?
What is the first thing you need to do in
order to determine the answer to the
question above?
“VISUALIZE THE PROBLEM”

## Slide 31: How many gallons of finished dilution of termiticide would you apply to treat the soil area to be covered by a slab that will be 40 feet wide by 150 feet long on a preconstruction treatment?
Draw a picture of the wall (a overhead view) to determine the area of
soil to be treated
150’
40’
150’
X 40’
6,000 sq. ft.

## Slide 32: How many gallons of finished dilution of termiticide would you apply to treat the soil area to be covered by a slab that will be 40 feet wide by 150 feet long on a preconstruction treatment?
What is the application rate to treat soil to be covered by a slab?
150’
40’
The rate of application to treat soil to be covered by a slab is 1 gal./10 sq. ft.
1 gal./10 sq. ft. = 0.1 gal./sq. ft.

## Slide 33: How many gallons of finished dilution of termiticide would you apply to treat the soil area to be covered by a slab that will be 40 feet wide by 150 feet long on a preconstruction treatment?
150’
40’
0.1 gal./sq.ft. X 6,000 square feet = 600 gallons of diluted termiticide
6,000 square feet
x0.1 gal./sq. ft.
600 gallons